## Slide 1
Session 4 Technical Drawings, Exploded View & BOM
Brief and practical checklist for what each team must create.
Convert the product into parts and assemblies.
Define what is manufactured vs. purchased.
Prepare the first BOM and drawing checklist.
Today: translate design intent into parts, drawings and a preliminary BOM.
Output: a report fragment ready to become part
of the final technical report.
Specification of Products and Services · Session 4

## Slide 2
Session goal
What must solve today.
02
What information would a manufacturer need to understand and produce your product?
1
1. Identify parts
List every piece, module, connector, textile piece, hardware item and consumable.
2
2. Organize assembly
Show how parts connect, open, fold, attach or are replaced.
3
3. Build the BOM
Create a preliminary list with quantities, materials, processes, suppliers and costs.
Output: practical technical documentation, not a final render.

## Slide 3
What to submit for Session 4
Keep it short, clear and advanced enough to integrate into the final report.
03
1
Product architecture
Parts, modules and how they work together.
2
Parts breakdown
Manufactured, commercial and consumable parts.
3
Exploded view
Sketch, CAD screenshot or diagram with labels.
4
Drawing checklist
Which drawings are needed for the final technical report.
5
Preliminary BOM
Quantity, material, process, supplier and estimated cost.
6
Assembly sequence
Basic order of construction or integration.
7
Risks + missing info
What still needs measurement, testing or supplier confirmation.
Suggested length: 6–10 pages. Use diagrams, tables and captions.

## Slide 4
Parts breakdown
Make the product visible as a system of pieces.
04
Manufactured parts
Custom pieces made for your project: • shells / bodies • textile or leather patterns • molded / printed components • custom pads or covers
Commercial parts
Purchased components: • buckles / zippers • screws / magnets • straps / webbing • electronics / batteries • hooks / latches
Consumables + finishes
Materials used during production: • adhesives • thread • coatings • labels • paint / dye • packaging
If a part exists in the product, it must appear in the parts list and later in the BOM.
Do not forget small items: thread, screws, labels, seals, adhesives and closures.

## Slide 5
Exploded view or assembly diagram
A sketch is acceptable if it clearly explains the product.
05
A01 outer shell / body
A02 support layer
A03 connector / strap
A04 base / interface
1
Must show
All main parts separated and labeled.
2
Must connect
Each label must match the BOM row.
3
Must clarify
How parts attach, move, fold, open or are replaced.
Use A01, A02, A03… and keep the same labels in drawings and BOM.

## Slide 6
Preliminary BOM
The BOM is the inventory of your product.
06
Part / Component
Qty.
Type
Material
Process / Supplier
Cost
Function
Status
Main shell / body
1
Manufactured
To define
3D print / injection / sewing
TBD
Main structure
needs dimensions
Strap / support
2
Commercial / manuf.
Nylon / textile
Supplier + stitching
TBD
Adjustment
needs test
Buckle / latch
1
Commercial
POM / metal
Supplier
TBD
Closure
choose type
Fasteners / thread
Several
Consumable
Steel / thread
Supplier
TBD
Assembly
count needed
Use “TBD / needs evidence” only when necessary. Do not leave empty cells.
Minimum: 10–15 rows depending on product complexity.

## Slide 7
Drawing checklist
Do not need perfect final drawings, just must know what to create.
07
General product drawing
Complete product + main dimensions
Part drawings
Individual pieces with dimensions
Assembly drawing
How parts fit together
Exploded view
Separated parts + labels
Detail drawing
Closures, joints or critical zones
Pattern / flat layout
Textile, leather, fabric or sheet products
Electronic diagram
Only if sensors, batteries or wiring exist

## Slide 8
What most teams need to improve
Based on the last submissions: be concrete and measurable.
08
1
Dimensions
Do not write only “to be defined”. Identify which dimensions are missing and why they matter.
2
Suppliers + costs
Start searching possible suppliers, commercial parts and price ranges.
3
Evidence
Plan tests: load, abrasion, water, magnets, comfort, assembly time or movement.
4
Clear diagrams
Include at least one labeled exploded view, pattern, sketch or assembly map.
5
Parts table
Every material decision must connect to a specific part or component.
6
Separate language
Technical report = production. Visual report = user understanding and purchase.
Goal: make the report useful for the final technical document.

## Slide 9
NotebookLM prompt for Session 4
Students can copy this and adapt it to their project.
09
Using only the uploaded sources, create a Session 4 report titled “Technical Drawings, Exploded View and Preliminary BOM”. Include: product architecture, parts breakdown, manufactured parts, commercial parts, exploded view description, drawing checklist, preliminary BOM, assembly sequence, technical risks, missing information and next steps. Create a BOM table with: Part / Component, Quantity, Type, Material, Process or Supplier, Estimated Cost, Function and Status. Do not invent final data. If information is missing, write “to be defined”, “needs measurement” or “needs evidence”.
NotebookLM creates a draft. Teams must edit, verify and add their own drawings and evidence.

## Slide 10
End-of-class output
By the end of Session 4, each team should leave with these four things.
10
1. Parts list
All pieces, modules, commercial parts and consumables.
2. First exploded view
Labeled sketch or CAD screenshot showing how parts connect.
3. Preliminary BOM
Rows with quantity, material, process, supplier/cost and status.
4. Drawing plan
List of drawings needed before the final technical report.
Session 4 is not about making perfect plans yet. It is about knowing exactly what must be drawn, bought, made and tested.
Next: ergonomics, validation, production manual and final documentation.